## Slide 1
Locking with the GHz
Frédéric BLANC
08/10/2021

## Slide 2: Summary
01
02
03
Setup
Results
Forecasts
[p.3]
[p.5]
[p.11]

## Slide 3: Setup
01

## Slide 4: Setup for GHz locking
04
Setup
Mirror
PhDs
PDH
Camera
EOM
Fiber
LASER
AOM
Lens
λ/4
Splitter
Combiner
λ/2
Polarizer
Unused (lock line)
GHz

## Slide 5: Results
02

## Slide 6: Lock GHz
06
Results
Error signal of the PDH, unlocked
Lock of the GHz

## Slide 7: Resonnance Piezo
07
Results
Phase noise and modulations.
We can see a peak at 30 kHz which produce these modulations.
Resonnance of the Piezo (30 kHz)

## Slide 8: Lock signal with 2 types of loop
08
Results
Differences between open loop and closed loop for motors on the cavity.
Peaks due to motors vibrations on close loop.

## Slide 9: Coupling and finess
09
Results
The coupling is around 20% (Green curve)
We measure the linewitdth between 879,67MHz and 880,1MHz, with a center frequency at 879,88MHz.
=> So the finess is around 2000.

## Slide 10: Beam imagery
10
Results
Beam in transmission

## Slide 11: Forecasts
03

## Slide 12: Forecasts
12
Forecasts
Phase noise measurement
Coupling the GHz with the Tangor
Align the Tangor with the cavity
Receive the lock line from Amplitude
1) GHz
2) Lock line

## Slide 15: Toolbox
Triangles
Coins de page
Bloc pour insérer des images
1
2
3
…
1
2
3
…
1
2
3
…