## Slide 1
Study of CSR impedance in ThomX with CSRZ code
Alexis Gamelin, Demin Zhou

## Slide 2
Coherent Synchrotron Radiation
G. Wüstefeld, BESSY, Short Bunches & CSR, EPAC‘08, June 23rd. 2008

## Slide 3
Popular models for CSR impedance
Free space CSR impedance
Parallel plate CSR impedance
For a point charge moving in free space on a circle of radius R, the steady state impedance is:

## Slide 4
Popular models for CSR impedance
Free space CSR impedance
Parallel plate CSR impedance
For a point charge moving in between two conducting plates in the horizontal plane on a circle of radius R, the steady state impedance is:
b

## Slide 5
Popular models for CSR impedance
These models neglects:
Transient effects
Transverse size of the beam
Transverse shielding
Resonant behavior
CSR interference
Reality is different from steady state model, in real machine dipoles are interleaved with drifts.
The vacuum chamber act as a waveguide and guided CSR fields can propagate along the beam.
The effect is also called « drift CSR »
Condition to neglect in ring:
With
Effect should be visible

## Slide 6
Popular models for CSR impedance
These models neglects:
Transient effects
Transverse size of the beam
Transverse shielding
Resonant behavior
CSR interference
Ring:
TL:
With
No effect
Condition to neglect:

## Slide 7
Popular models for CSR impedance
These models neglects:
Transient effects
Transverse size of the beam
Transverse shielding
Resonant behavior
CSR interference
Reflection on outer wall -> Head-Tail effect
Reflection on inner wall -> Tail-Head effect
Geometric condition to neglect in the ring:
Outer walls ->
Inner walls ->
At injection:
Effect should be visible

## Slide 8
Popular models for CSR impedance
These models neglects:
Transient effects
Transverse size of the beam
Transverse shielding
Resonant behavior
CSR interference
For long dipole chambers, some modes can be strongly excited by the beam and dominate the CSR impedance
Condition to neglect in ring:
Effect should be visible
Distance between vertical walls

## Slide 9
Popular models for CSR impedance
These models neglects:
Transient effects
Transverse size of the beam
Transverse shielding
Resonant behavior
CSR interference
CSR fields emitted in each dipoles can interact and interfere
Condition to neglect in ring -> ? (depends on geometry)

## Slide 10
CSRZ code by Demin Zhou
Compute the CSR impedance by numerical integration of Maxwell equations in the paraxial approximation
For a rectangular beam pipe on arbitrary trajectory
Assume Gaussian bunches
Input file:
Zmethod = 1 -> integration end at fixed position
Zmethod = 2 -> integration to infinite length

## Slide 11
ThomX ring: 1 bend
Effect of shielding CSR -> Add a threshold
~47 GHz

## Slide 12
ThomX ring: 1 bend
Resonant behavior
Transiant effects

## Slide 13
ThomX ring: 1 bend
For:
Parallel plate CSR
Rectangular chamber CSR
Inner wall: negligeable
Outer wall and resonances
Transient effects

## Slide 14
ThomX ring: 2 bend
CSR impedance of 2 bend divided by 2 for comparison
Constructive interference
Destructive interference

## Slide 15
ThomX ring: 3 bend

## Slide 16
ThomX ring: 4 bend

## Slide 17
ThomX ring: 4 bend
For:
Parallel plate CSR
Rectangular chamber CSR
Interferences

## Slide 18
ThomX ring: Full ring
Computation running for 650h
According to Demin Zhou: this type of spectrum has been measured experimentally with THz monitors -> real effect

## Slide 19
Why should we care : impact on beam dynamics
Total energy loss per bunch

## Slide 20
ThomX ring: 4 bend
For:
Parallel plate CSR
Rectangular chamber CSR
Peak amplitude x 15 compared to

## Slide 21
Why should we care : impact on beam dynamics
In ThomX -> Injection without longitudinal matching
With CSR PP, space charge and impedance
1000 tours
Bunch at injection :
Charge = 100 pC
6,6 ps
= 0,2 %
Quick filamentation
With CSR PP, space charge and impedance
1000 tours
Bunch quickly fill the RF acceptance

## Slide 22
Why should we care : impact on beam dynamics
Bunch at injection :
Charge = 100 pC
6,6 ps
= 0,2 %
Toy simulation 10 000 particles with CSR PP
100 tours
Beam not Gaussian in longitudinal
Head-Tail and Tail-Head effets important !

## Slide 23
Why should we care : impact on beam dynamics
With CSR PP, space charge and impedance
1000 tours
Bunch at injection :
Charge = 1 nC
6,6 ps
= 0,2 %
Bunch splits in 3 parts
CSR instability
With CSR PP, space charge and impedance
1000 tours
CSR ∝ N2

## Slide 24
Why should we care : impact on beam dynamics
Bunch at injection :
Charge = 1 nC
6,6 ps
= 0,2 %
Toy simulation 10 000 particles with CSR PP
100 tours
Beam not Gaussian in longitudinal
Head-Tail and Tail-Head effets important !

## Slide 25
Micro Wave Instability (MWI)
MWI threshold driven by CSR PP:
With:

## Slide 26
TL 2 bend model
Parallel plate CSR
Rectangular chamber CSR

## Slide 27
TL 2 bend model
Parallel plate CSR
Rectangular chamber CSR

## Slide 28
TL 4 bend model
Parallel plate CSR
Rectangular chamber CSR

## Slide 29
TL 4 bend model
Parallel plate CSR
Rectangular chamber CSR